| IP xy degree of protection |
| --- |
| Dust proof (x) | Water proof (y) |
| 0. No protection 1. Protection against solid foreign object >50mm. 2. Protection against solid foreign object >12mm. 3. Protection against solid foreign object >2.5mm. 4. Protection against solid foreign object >1mm. 5. Dust protected 6. Dust tight | 0. No protection 1. Protection against vertically falling water. 2. Protection against vertically falling water when the enclosure is tilted up 15 degrees. 3. Protection against spraying water (tilted 60 degrees). 4. Protection against splashing water. 5. Protection against water jet (12.5L/minute). 6. Protection against powerful water jet (100L/minute). 7. Protection against temporary immersion in water (30 minutes, 1m below surface). 8. Protection against continuous immersion in water (conditions to be defined by manufacturer and buyer). |